## Slide 1
Welcome
These challenges were developed by Derrick Willer MBE and colleagues.
They are free to download and use in an education environment.
Please ensure that there is adult supervision, complete adherence to Health and Safety, and adequate PPE.
Derrick is a STEM Ambassador.
He has supported education in schools and colleges for over 30 years, initially as a Neighbourhood Engineer in the 1980’s, leading the local Year of Engineering Success campaign in 1996 and the Campaign to Promote Engineering from 1997 to 2004.
He was awarded an MBE for services to Education in 2018.

## Slide 2
Guide
This activity is for pupils to understand various logic and maths questions.
Risks
Item | Risk | Avoidance Action
Batteries | Injury | Close supervision. Circuits to be checked before allowing participant to switch on. Beware short circuiting the batteries, risk of fire and burning.
Micro-bit | Damage | Close supervision. Circuits to be checked before allowing participant to switch on.
Aggression between participants | Injury | Close supervision and immediate action to defuse aggression
Mandatory: close supervision by a competent adult

## Slide 3
Make
Traffic Lights With BBC Micro-bit

## Slide 4
Connect the buzzer between 0 and GND
Intermittent Buzzer
First let’s try a simple circuit with a buzzer using Python programming language

## Slide 5
from microbit import *
while True:
pin0.write_digital(1)
sleep(20)
pin0.write_digital(0)
sleep(480)
Connect the buzzer between 0 and GND
The device is put into an infinite loop and immediately switches pin 0 on. This causes the speaker to emit a beep. While the speaker is beeping, the device sleeps for twenty milliseconds and then switches pin 0 off. This gives the effect of a short bleep. Finally, the device sleeps for 480 milliseconds before looping back and starting all over again. This means you’ll get two bleeps per second (one every 500 milliseconds).
Python Code
Intermittent Buzzer

## Slide 6
UK Traffic Lights – Just One Set
Now let’s try a single Traffic Light set
Can you write the Python Code for this?

## Slide 7
from microbit import *
while True:
pin0.write_digital(1)
sleep(15000)
pin1.write_digital(1)
sleep(7000)
pin0.write_digital(0)
pin1.write_digital(0)
pin2.write_digital(1)
sleep(15000)
pin1.write_digial(1)
pin2.write_digital(0)
sleep(7000)
pin1.write_digital(0)
Python Code
UK Traffic Lights – Just One Set
Red on for 15 seconds
Red and Yellow for 7 seconds
Green for 15 seconds
Yellow for 7 seconds
Then start again

## Slide 8
Cross Roads have opposite lights but you cannot assume if the North-South Red is on the opposite East-West Green is on.
Cross Roads Traffic Lights
North-South Sequence
East-West Sequence
1 2 3 4
1 2 3 4

## Slide 9
Sequence | Red | Yellow | Green | Red | Yellow | Green
1 | On |  |  |  |  | On
2 | On | On |  |  | On | 
3 |  |  | On | On |  | 
4 |  | On |  | On | On | 
The Traffic Light Sequence is:
Cross Roads have opposite lights but you cannot assume if the North-South Red is on the opposite East-West Green is on
Cross Roads
We need Four Conditions but the BBC-Micro-bit only gives Three outputs! Can you think of a solution?

## Slide 10
Sequence | Red | Yellow | Green | Red | Yellow | Green
1 | On |  |  |  |  | On
2 | On | On |  |  | On | 
3 |  |  | On | On |  | 
4 |  | On |  | On | On | 
The Traffic Light Sequence is:
Cross Roads
We need Four Conditions but the BBC-Micro-bit only gives Three outputs! Can you think of a solution?
Whenever any Yellow Light is ON – all the Green Lights are OFF !!
In fact the Yellow Lights are always ON together

## Slide 11
Sequence | Red | Yellow | Green | Red | Yellow | Green
1 | On |  |  |  |  | On
2 | On | On |  |  | On | 
3 |  |  | On | On |  | 
4 |  | On |  | On | On | 
The Traffic Light Sequence is:
Cross Roads
Whenever any Yellow Light is ON – all the Green Lights are OFF !!
We need a switch which is OFF if the Yellow Lights are ON

## Slide 12
Cross Roads
Whenever any Yellow Light is ON – all the Green Lights are OFF !!
We need a switch which is OFF if the Yellow Lights are ON
Lets try a relay!
When the current flows the Green Contact is Broken = OFF
Coil
+3V
0V
Magnetic
Contact
Green Lights
Normally Closed Terminal
Common
Terminal

## Slide 13
Diodes
We need Diodes to stop the current from the Red going to light the Green when the Yellow is on

## Slide 14
Diodes
Normally Closed
Now lets see the circuit with the Relay in place
Normally Open
Common
Coil
Terminals
Return

## Slide 15
`
Diodes
Now for the Python Code
from microbit import *
while True:
pin0.write_digital(1)
sleep(15000)
pin0.write_digital(0)
pin1.write_digital(1)
sleep(7000)
pin1.write_digital(0)
pin2.write_digital(1)
sleep(15000)
pin2.write_digital(0)
pin3.write_digial(1)
sleep(7000)
pin3.write_digital(0)
NS Red and EW Green on for 15 seconds
NS Red and both Yellows ON for 7 seconds, Relay ON and turns All Green OFF
EW Red ON and NS Green ON for 15 seconds
EW Red and both Yellows ON for 7 seconds, Relay ON and turns All Green Off
Then start again

## Slide 16
Now for the Python Code
from microbit import *
while True:
pin0.write_digital(1)
sleep(15000)
pin0.write_digital(0)
pin1.write_digital(1)
sleep(7000)
pin1.write_digital(0)
pin2.write_digital(1)
sleep(15000)
pin2.write_digital(0)
pin3.write_digial(1)
sleep(7000)
pin3.write_digital(0)
NS Red and EW Green on for 15 seconds
NS Red and both Yellows ON for 7 seconds, Relay ON and turns All Green OFF
EW Red ON and NS Green ON for 15 seconds
EW Red and both Yellows ON for 7 seconds, Relay ON and turns All Green Off
Then start again
Q.E.D.
Quite Easily Done
No!
Quad Erat Demonstrandum

## Slide 17
Now lets make the Traffic Lights out of Recycled Materials

## Slide 18: We have learnt to:
Work and think as engineers
Understand BBC Micro-bit
Understand Python Programming
Understand Electric Circuits
Work as a team
Build with the resources available

## Slide 20
Thank You

## Slide 21
These challenges were developed by Derrick Willer MBE and colleagues.
They are free to download and use.
Please ensure that there is adult supervision, complete adherence to Health and Safety, and adequate PPE.
Derrick is a STEM Ambassador and volunteer Schools Liaison Officer for the IET Coventry and Warwickshire Network.
He has supported education in schools and colleges for some 30 years, initially as a Neighbourhood Engineer in the 1980’s, leading the local Year of Engineering Success campaign in 1996 and the Campaign to Promote Engineering from 1997 to 2004.
Derrick was awarded an MBE for services to Education in 2019.

## Slide 23
BBC Micro-bit (e.g. Kitronic)
LEDs 2 Red, 2 Yellow, 2 Green
(e.g. Kitronic, Amazon)
Diodes – 6
(e.g. Kitronic, Amazon)
Relay – 1
(e.g. Kitronic, Amazon)
Buzzer 3V+ - 1
(e.g. Kitronic, Amazon)
Crocodile Clips – 20
(e.g. Kitronic, Amazon)
Wire – Multicolours Male to Male
Materials